## Slide 1: Vietnam to Produce More Coffee With Less Water
Date: July 19th, 2016
Venue: Buon Ma Thuot, Dak Lak, Vietnam
Authors: Dr. Ellen Milnes
Dr. Francois Negro
Msc. Stephan Studer
Dr. Dave D‘haeze
Prof. Pierre Perrochet
Towards a Reduction of the
Blue Water Footprint
in Coffee Production
Hydrogeological Study on the Dak Lak Basaltic Plateau Towards modern watershed monitoring & management

## Slide 2: Overview
Rationale
Objectives
Potential Impact
Results
Conclusions
Recommendations
Water Monitoring Strategy
Next steps

## Slide 3: Rationale
Global coffee demand is increasing while productivity in Vietnam may potentially decline, despite
  Rejuvenation programs & new high yielding varieties
Production in Vietnam is at risk
  Looming water scarcity & climate change
Irrigation water is a pre-condition to make coffee production economically viable
  Current average 2.3 Mt/ha; potential 4 Mt/ha
Current irrigation practices are unsustainable and endanger
  Coffee productivity
  Household water supply
  Hydro-power generation
  Production of other water demanding (food) crops
  Current irrigation practices for coffee can be reduced by at least 30%
  Government recognition importance of water for coffee (cf. Nestle-SDC policy brief, 2013)
  Vietnamese request for larger scale interventions
  Current momentum should not be missed

## Slide 4: Objectives
Overall Objective
  Equitable and sufficient water availability for all water users in the Central Highlands
  Pivotal water savings through improved irrigation management in the coffee sector
  Improved people’s livelihoods in socio-economic terms and environmental protection
  Specific Objective 1 Water resources management is improved
  Water supply and demand inventoried in Dak Lak province
  Impact of coffee production on water resources assessed
  Water scarce hotspots identified
  Water Action Plans formulated, implemented and monitored for 2 pilot micro-catchments
Specific Objective 2 A weather early warning system supports optimization of coffee farm management
  A weather early warning system designed, tested and implemented for one Central Highland’s province in order to support optimization of farm management.

## Slide 5: Objectives
  Specific Objective 3 Scaling up through farmer trainings
  50,000 small-scale and poorer farmers deprived of information, in the 5 main coffee producing provinces produce coffee in an economically and particularly water efficient manner
  Access to improved technological support with regard to water management and GAP for Robusta production which leads to important water savings in agriculture
Specific Objective 4 Policy advocacy
  The project is a concrete model featuring the subject of water efficiency in international policy debates
  Relevant policy makers have been sensitized through the project’s results
.
.
Ha Noi
Ho Chi Minh
Dak Nong
Kon Tum
Dak Lak
Gia Lai
Lam Dong

## Slide 6: Potential Impact
Water for annual household consumption available for 25 million water users (28% National population)
  Assume 120 liter per day per capita for household use
  500,000 (100%) coffee growers reduce irrigation
  1,000 (conventional irrigation practice)  400 liter/tree/round (-60%)
  Absolute water savings of 1 billion m3
  If all coffee farmers adopt Best Irrigation Practices

## Slide 7: Results: Two-Step Approach
Provincial scale
  What is the large scale potential water availability in Dak Lak province?
  Are there potential water scarce “hot-spots” for irrigated coffee production?
Basaltic plateau scale
  Has any long-term groundwater decline been observed?
  Does excessive irrigation water replenish the groundwater within the current dry season?
  Where are high risk areas prone to drying up of wells and what are the reasons?
  Best irrigation practices for coffee - a solution to avoid seasonal drying up of shallow wells?

## Slide 8: Results: Provincial Scale -Aquifer types
From geology to hydrogeology
  Identification of rock types in terms of hydraulic properties and spatial distribution
    5 geological units in Dak Lak
    Basaltic plateau is the largest continuous aquifer system
Fractured weathered basalt
Weathered basalt
Granite
Basaltic plateau

## Slide 9: Results: Provincial Scale - Land Use Mapping
Land Use
  18.5% of Dak Lak is covered with coffee
  86% of coffee on the basaltic plateau
Strong correlation between land use and geology
  Coffee plantations are concentrated on the basaltic plateau
Forest
Paddy rice
Robusta coffee

## Slide 10: Results: Provincial Scale - Water balance
`
Annual Average Water Balance (P – ET )
  Provincial average annual rainfall: 1,300 – 2,000 mm/year
  Lowest annual rainfall: lowest altitudes (NW Dak Lak) & eastern basaltic plateau.
  Highest evapotranspiration: forest areas (south-east) & coffee areas (central basaltic plateau)
  3 low potential water-availability areas:
    Eastern half basaltic plateau: highly evaporative coffee plantations & lower rainfall
    North-west: forests
    South-east: forests
2
1
3

## Slide 11: Results: Provincial Scale - Water Scarce Hot Spots
Potential Annual Average Water Deficit
  Deducting dry-season water requirements (irrigation) from the annual water availability map
  Highest risk areas:
    irrigated coffee on the eastern half of the basaltic plateau
    paddy rice
    forest areas in the northwest
  Current coffee irrigation practices may pose a higher risk compared to best practices:
    in the dry season (seasonal issue)
    on the basaltic plateau
1
1

## Slide 12: Results: Basaltic Plateau Scale - Water level analysis
  Long-term groundwater level analysis
  Stable groundwater body
    No historic large-scale declining water level trends
    Groundwater recharge in rainy season replenishes water extractions in dry season
  No long-term historic
  groundwater level decline
LK71
LK29
LK30
LK49
LK70
CB1-II
LK69
C4o
  E.g. borehole C4a (border Krong Pach and Krong Buk); increased water level fluctuation since 2003, no water level decline
2001
2014
1993
2010
2003

## Slide 13: Results: Basaltic Plateau Scale - Water level analysis
  Seasonal groundwater level analysis
  Seasonal groundwater recharge takes place 60-100 days after onset of rainy season (in areas with unsaturated zone > 15m)
  Water level fluctuation amplitudes are correlated by order of importance with:
    the thickness of the unsaturated zone (related to the relative topographical position)
    the distance to the closest discharge area (spring, stream, lake, river)
Time lag (days)
Onset recharge
Onset rainy season
Monitoring borehole CB4-II: long term
Monitoring borehole CB4-II: close up

## Slide 14: Results: Basaltic Plateau Scale - Water level analysis
  Event groundwater level analysis
  Extreme rain event within the rainy season (August 2007); 600 mm of rainfall in 6 days
    Wet soil
     Deep percolation reaches groundwater within 10 days (depending on soil thickness and hydraulic properties)
  Rainfall event end dry season (April 2007); 83 mm of rainfall in 3 days, similar to an irrigation event
    Dry soil
     Deep percolation does not reach groundwater within the dry season, as groundwater levels continue to decline (until early May)
  Excess water from over-irrigation temporary retained in the unsaturated soil column
30 July
01 September
12 April
15 May
LK29 (15m)
C8b (4m)
Rainy season; wet soil
C8b (4m)
LK29 (15m)
Water level change since event start (m)
Dry season; dry soil
Similar to irrigation event

## Slide 15: Results: Basaltic Plateau Scale - Areas at risk of running dry
Unsaturated zone exceeding shallow aquifer thickness
Shallow aquifer water bearing
Shallow aquifer pressurized; artesian conditions
Unsaturated soil thickness
Hydraulic head distribution
Pressurised area (artesian)
Lake
Calibration
Computed heads (masl)
Measured average water level (masl)
  3D numerical model to map the spatial distribution of the area at risk of running dry from a hydrodynamic perspective
  Unsaturated zone exceeding the shallow aquifer thickness of 30 meters

## Slide 16
  Areas with high topography (relative) & far from local discharge areas
  Water table depth > 30 m  shallow aquifer dry
2. Unsaturated soil thickness >30m
Unsaturated zone exceeding shallow aquifer thickness
Shallow aquifer water bearing
Shallow aquifer pressurized; artesian conditions
Results: Basaltic Plateau Scale - Dry area risk maps
Unsaturated soil thickness

## Slide 17: Results: Basaltic Plateau Scale - Groundwater recharge
  Spatial groundwater recharge distribution
  Surface water runoff and base flow were obtained from hydrograph separation (for Krong Buk catchment and extrapolated to the basalt plateau)
  Groundwater recharge =
  Rainfall – Evapotranspiration – Surface
  Runoff
  Groundwater recharge in the West almost double than in the East (because of rainfall):
    West : 500 - 900 mm/year
    East: 300 - 500 mm/year
Average recharge
(mm/year)

## Slide 18
  Results: Basaltic Plateau Scale -
  Water scarcity
  Irrigation extractions vs. groundwater recharge (Q/I)
  Irrigation extractions (Q) take place during the dry season and groundwater recharge (I) mainly during the rainy season
  Ratio (Q/I) reveals the spatial distribution of water scarcity, accounting for seasonal effects
   Current irrigation practices
    Groundwater extraction (Q) is 50 – 100% of annual renewable groundwater recharge (I) in many areas
   Best irrigation practices
    Groundwater extraction (Q) is mostly 20 – 40% of annual renewable groundwater recharge (I)
Irrigation vs. groundwater recharge (%)
Current Irrigation Practice
Best Irrigation Practice

## Slide 19: Results: Basaltic Plateau Scale - Water scarcity maps
  Areas with low water availability
  Irrigation extraction > 50% annual renewable groundwater recharge
Ratio irrigation vs. recharge (%)
1. Ratio irrigation vs. recharge >50%

## Slide 20
2. Unsaturated soil thickness >30m
1. Ratio irrigation vs. recharge >50%
Water scarce hot spots:
Combination 1 * 2
x
=
  Water scarce hotspots combined effect of low water availability and risk of running dry
  Map overlay of:
  Irrigation extraction > 50% annual renewable groundwater recharge
  Areas with high topography (relative) & far from local discharge area
    Unsaturated soil thickness > 30 m
Results: Basaltic Plateau Scale - Water scarce hot spots

## Slide 21
Conclusions
  Provincial scale
  Strong correlation between land use and geology: 86% of provincial coffee production on basaltic plateau
  Water scarce hot spots are mainly in irrigated coffee areas on the eastern half of the basaltic plateau
  Current coffee irrigation practices lead to higher water scarcity as compared to recommended best practices in the dry season
  Basaltic plateau scale
  No long-term declining water level trends observed
  Water level decline during the dry season is responsible for running dry of shallow wells and is correlated with:
    the location of the well
    the irrigation practices
  Excess irrigation water is temporarily trapped in the soil and is not available for use during the dry season
  Water scarce hot spots are concentrated in the higher altitudes of the plateau and in the East (Krong Buk, Buon Ho, Krong Nang).

## Slide 22
  Changing the irrigation practices from conventional to best practices to reduce the risk of wells drying up, with special focus on water scarce hot spots where the impact is biggest
  Monitoring of water-scarce micro-catchments to assess the impact of the irrigation practices on the water resources
  Up-scaling of method to map water scarce hot spots could be applied to other basaltic plateaus in the Central Highlands with similar characteristics
Recommendations

## Slide 23
  Quantify the impact of changing irrigation volumes for coffee, from actual state to best practices by high-resolution monitoring of
  Groundwater levels,
  Catchment run-off,
  Soil moisture,
  Rainfall; and
  Evapotranspiration.
  Introduce local stakeholders to new, modern water monitoring technology
Identify and actively involve local stakeholders in
  Data collection,
  Data analysis,
  Data interpretation; and
  Policy formulation.
Water Monitoring Strategy -
Objectives

## Slide 24
Criteria
  Water-scarce hot spots, as obtained from the base-line study
  Within the two approved districts (Kronk Buk and Krong Nang)
  Accessibility
  Willingness of farmers
  Areas, where farmer training is planned
  No state farms (as they usually have access to surface water tapped from reservoirs)
Field Survey
  Surveying 19 shallow wells, 1 borehole and 2 springs
  Size of micro-catchment: 1 km2
Water Monitoring Strategy -
Catchment Selection
1
2
3

## Slide 25
  Quantifying
Water Monitoring Strategy -
Monitoring Setup

## Slide 26: Next steps
Next steps
  Identify local partners to actively conduct water monitoring, analysis and reporting
  Identify a PhD student to join the project and elaborate further on the initial findings of CHYN University
  Sketch the current water management procedures in the Central Highlands/Vietnam and identify redundancies/gaps
    Who is responsible for what?
    Who collects which data?
    Who consolidates data?
    Who reports to whom?
    Who is in charge of data analysis and policy formulation?

## Slide 27: Thanks for your attention
Embden, Drishaus & Epping Consulting GmbH
Representative Office Asia Pacific
90 Tran Nhat Duat, Tan Loi Ward, Buon Ma Thuot, Dak Lak, Vietnam
Phone +84 (0)5003 976 667
Fax: +84 (0)5003 976 668
dave.dhaeze@ede-consulting.com
Dothanh.chung@ede-consulting.com